## Slide 1
THE DRAKKAR ASCENT CHALLENGE
Design Review Board — Structural Optimization of Booster Thrust Barrel
Cadre: Lockheed Martian | Course: Aircraft Structures (R5ME3203T) | VJTI Mumbai
Engineering Cadre Members: • Aryan Vyapari (241030078) • Ashutosh Yadav (241030079) • Rishiraj Rajgore (241030067) • Archit More (241030057)

## Slide 2
THE DRAKKAR ASCENT CHALLENGE | HOUSE VERIDIAN
Mission Envelope & Applied Flight Loads
• Ascent Flight Condition: Max dynamic pressure q = 24.5 kPa at V_inf = 200 m/s with severe 20 m/s vertical desert thermal gust.
• Team Adopted Design Factor: LF = 1.1 applied once directly to all primary flight forces and pressure before second-order analysis.
• Axial Engine Compression: F = 30.0 kN service --> 33.0 kN design thrust transmitted axially through the cylindrical shell.
• Propellant Tank Ullage Pressure: p = 0.30 MPa service --> 0.33 MPa design wall pressure (no beneficial pressure stabilization credited in buckling).
• Aerodynamic Gust Side Loads: Shear V = 1,465.1 N --> 1,611.6 N design; First-order Bending M_0 = 2,197.7 N.m --> 2,417.5 N.m design.
• Beam-Column Amplified Moment: P-delta moment magnification: M_design = 3,027.9 N.m (amplification factor = 1.252).

## Slide 3
THE DRAKKAR ASCENT CHALLENGE | HOUSE VERIDIAN
Theoretical Analysis Architecture (No FEA)
• Exact Annular Geometry: Exact midsurface radius r = (D - t)/2, area A = pi*(ro^2 - ri^2), and moment of inertia I = (pi/4)*(ro^4 - ri^4).
• Second-Order Beam-Column Secant: Exact pinned beam-column solution M_design = M_0 / cos[(L/2)*sqrt(P/EI)] eliminates heuristic P_eq approximations.
• Co-Located Stress Envelope: Evaluates signed axial compression, outer-fiber bending, hoop tension, and shear at identical circumferential positions (theta = 180 deg governs).
• NASA SP-8007 Shell Buckling: Empirical curvature knockdowns gx and gb as continuous functions of sqrt(r/t)/16 (gx = 0.651, gb = 0.717).
• Combined Stability Interaction: Tri-axial interaction criterion: (sigma_axial/sx_cr) + (sigma_bending/sb_cr) + (tau/tau_cr) <= 1.0.
• Brazier Ovalization Diagnostic: Classical elastic tube flattening capacity M_Brazier = 0.987*E*r*t^2/sqrt(1 - nu^2) evaluated at midspan.

## Slide 4
THE DRAKKAR ASCENT CHALLENGE | HOUSE VERIDIAN
Parametric Material Trade Study (LF = 1.1)
Material | Class | Optimum OD | Wall (t) | Shell Mass | Status / Selection
Aluminium 7075-T6 | Metal | 119 mm | 0.96 mm | 1.501 kg | PRIMARY SELECTED WINNER
Magnesium AZ31B | Metal | 169 mm | 1.10 mm | 1.540 kg | Heavier (+2.6%, yield cap)
Titanium Ti-6Al-4V | Metal | 96 mm | 0.84 mm | 1.669 kg | Dense (+11.2%)
Steel 4130 | Metal | 154 mm | 0.58 mm | 3.292 kg | Heavy (+119.3%)
Carbon/Epoxy QI | Composite | 101 mm | 1.20 mm | 0.903 kg | Theoretical min (unvalidated)
Aramid/Epoxy QI | Composite | 169 mm | 1.23 mm | 1.361 kg | Laminate unvalidated
Glass/Epoxy QI | Composite | 125 mm | 1.60 mm | 1.768 kg | Laminate unvalidated
Why Aluminium 7075-T6 Wins Over Magnesium and Composites:
1. High stiffness (71.7 GPa) and yield strength (503 MPa) prevent early buckling limits, beating Magnesium AZ31B (1.540 kg) by 2.6%. 2. Carbon/Epoxy QI is theoretically lighter (0.903 kg), but the brief lacks laminate ply schedules, curing specifications, and delamination knockdowns required for certified aerospace production.

## Slide 5
THE DRAKKAR ASCENT CHALLENGE | HOUSE VERIDIAN
Final Architecture: Aluminium 7075-T6 Thrust Barrel
• Physical Dimensions: Outside Diameter = 119 mm | Nominal Wall = 0.96 mm | Length = 1500 mm | Mean Radius r = 59.02 mm.
• Component Mass: Shell Mass = 1.500541 kg (~1.501 kg). Valid thin-walled cylinder: r/t = 61.5, L/r = 25.4.
• Local Shell Buckling (GOVERNS): Interaction Utilisation U = 0.9962 (Margin of Safety = +0.38%). Directly sizes nominal wall thickness.
• Material Yielding Check: Peak von Mises Stress = 393.9 MPa <= 503.0 MPa allowable. Utilisation U = 0.7830 (Margin of Safety = +27.7%).
• Global Column Euler Buckling: Critical Euler Thrust P_cr = 195.0 kN >> 33.0 kN design load. Utilisation U = 0.1692 (Margin of Safety = +491%).
• Cross-Section Ovalization: Max Bending Moment = 3,027.9 N.m < M_Brazier = 4,077.7 N.m. Utilisation U = 0.7425 (Margin of Safety = +34.7%).
• Separate Transfer Load Case: Carrying shear across length (M + V*L = 4,835 N.m) yields OD = 137 mm, t = 1.10 mm, Mass = 1.980 kg.

## Slide 6
THE DRAKKAR ASCENT CHALLENGE | HOUSE VERIDIAN
Independent Verification & Compliance Summary
• 100% Automated Test Suite Passing: All 16 unit tests in tests/test_analysis.py pass in 0.02s, validating flight load derivations, known annular formulas, and trade studies.
• Independent Closed-Form Arithmetic: Full N/mm/MPa recalculation reproduces 14 finalist designs and 35 load scenarios with relative moment error < 1.56e-11.
• Dense Circumferential Scan: Co-located multi-axial stresses independently verified across 7,200 angular increments around cylinder perimeter.
• Academic Limitations Honestly Declared: NASA axial knockdown extrapolated for L/r = 25.4 > 5; end ring fitting mass separated from shell mass boundary.
• Submission Deliverables Ready: 1. Final Design Report (PDF) | 2. Python Code & Tests | 3. 2D CAD Engineering Drawing | 4. Presentation Slides.